Documentation -TFKISS- TheFirmware TNC Software Emulator
--------------------------------------------------------
by Mark Wahl, DL4YBG (last change: 20.10.96)


0. Introduction
---------------
0.1. Licenses
-------------
TFKISS is based on TheFirmware by NORD><LINK, license policy given by
'copyrght.txt' in this archive. ALAS is a german license for ham radio
software.
Most everything of the AXIP-interface is taken from AX25IP written by
Mike Westerhof KA9WSB. His copyright notice is given below:
>-------------------------------------------------------------------------
>Copyright 1991, Michael Westerhof, Sun Microsystems, Inc.
>This software may be freely used, distributed, or modified, providing
>this footer is not removed.
>-------------------------------------------------------------------------
The PID change code was written together with Joachim, DL8HBS.
The FLEXNET decoding code was written by Rene, DG0FT.
The other code and all adaptions are written by me. I put this code
under license policy of ALAS, too.

0.2. Description
----------------
TNT, my hostmode terminal program needs a TNC with TheFirmware connected
on a serial interface. There are some applications, where other
configurations are needed:
- The TNC or PR-controller software is not compatible to TheFirmware and
  its hostmode, but does support KISS mode
- The interface is not on a HF-frequency, but a TCP/IP-based network
  (local net or internet)
- TNT together with DPBox shall be used directly connected to a digipeater
  using KISS mode (hopefully with CRC) as interface

To handle these applications, TFKISS was written. It is in fact a porting
of the original TheFirmware by NORD><LINK, written for TNC2-hardware.
The low level interfaces were changed and adapted to Linux. On the
radio side a KISS- and an AXIP-interface take the place of the HDLC/modem
interface. The host connection is changed to a direct console interface (for
terminal mode) and a socket interface (for TNT).


1. Configuration
----------------
It is possible to operate TFKISS in several combinations. The radio side
can be a KISS interface, an AXIP interface or a combination of both.
On the host side a simple terminal mode can be used (nice for first tests)
or a socket interface to work together with TNT.

1.1. General configuration (tfkiss.ini)
---------------------------------------
This file is searched in the current directory and if not found in the
home directory of the user.
Here is a description of parameters which can be defined in the main
configuration file.

a) general parameters
- kiss_active		must be set to 1, if KISS interface shall be used,
			otherwise set to 0.
- axip_active		must be set to 1, if AXIP interface shall be used,
			otherwise set to 0.
- tfkiss_dir		directory path where all tfkiss files, configuration
			and data/log files will be stored.
- tfkiss_procfile	name of file containing the process id of the running
			TFKISS process (for use with BOXSTART).
- tfkiss_errfile	name for logfile to which logging data, warning and
			error messages will be saved.
- tfkiss_parafile	name of file where TFKISS will store internal para-
			meters (callsign, txdelay, e.t.c.) at termination.

Only one of the following values is allowed:

- tfkiss_socket		defines name of socket which is used as an interface
			to TNT. The socket is defined by a valid pathname.
			If the name does not start with a '/', 'tfkiss_dir'
			is added at the beginning.
- tfkiss_extsocket	defines name of socket which is used as an interface
			to TNT. The socket can be an UNIX- or an IP-Socket.
			Unix-sockets are defined by 'unix:<pathname>',
			IP-Sockets by <IP-address/name>:<portnumber>.
			Valid examples are:
				unix:tfkiss
				unix:/usr/local/dptnt/tfkiss/tfkiss
				*:5000
				localhost:5002
				bla.blub.org:6000

If both tfkiss_socket and tfkiss_extsocket are left blank, TFKISS will start
in terminal mode on the console.

b) parameters for KISS interface
- device		device used for a KISS interface, a serial device or
			any other tty-device.
- tfkiss_lockfile	lockfile to lock the KISS device against other
                        programs.
- speed			baudrate used on KISS device
- fulldup_on_dama	set to 1 for better DAMA performance, allows a quick
			answer on the poll of the DAMA master independent of
			DCD.
- kisstype		type of KISS which shall be used on KISS device:
			0: normal KISS without CRC
			   WARNING: This is HIGHLY insecure! You may lose
			   characters on the serial line WITHOUT knowing it.
			   Use this only for testing purposes!
			1: SMACK, KISS with CRC16, developed by
			   Jan Schiefer, DL5UE
			2: RMNC-KISS, KISS with CRC as implemented in
			   FLEXNET digipeater software
			Note: There is NO autoprobing of the protocol
			of the connected KISS device. You have to select
			the correct mode manually!

c) parameters for AXIP interface
- tfkiss_axipconfig	name of file which will contain all parameters
			concerning AXIP configuration.

Sample tfkiss.ini file:
# enable (1) or disable (0) kiss port
kiss_active 1
# enable (1) or disable (0) axip port
axip_active 0
# device for kiss port
device /dev/cua0
# lockfile for device used for kiss port
tfkiss_lockfile /usr/spool/uucp/LCK..cua0
# speed on device for kiss port
speed 19200
# switch kiss-tnc to fullduplex if DAMA detected
fulldup_on_dama 1
# directory for config/status files
tfkiss_dir /work/tfkiss
# file containing process id
tfkiss_procfile tfkiss.pid
# log file for errors
tfkiss_errfile tfkiss.err
# save file for parameters
tfkiss_parafile tfkiss.par
# UNIX-socket for connection to TNT
tfkiss_socket socket
# config-file for axip port
tfkiss_axipconfig tfkiss.cfg
# type of KISS on kiss port: 0: KISS, 1: SMACK, 2: RMNC-KISS
kisstype 1
<EOF>

1.2. AXIP configuration (tfkiss.cfg)
------------------------------------
All AXIP configuration is defined in this file, which layout is similar
to that of the original AX25IP program:

- socket		give mode of operation, several entries are
			possible.
			ip: AXIP according to RFC1226
			udp: transport of AX25 data via an udp connection,
			     if no port is given, 10093 is used as a
			     default.

- mode			defines the mode of operation of the AXIP part
			of TFKISS.
			tnc: data is given transparently to/from network
			digi: data is digipeated using call defined as
			      mycall

- mycall		digipeater callsign, only needed if mode digi is
			used.

- loglevel		logging function for debugging purposes, logging
			data will be put to file defined by tfkiss_errfile.

- route			defines routing data, gives network destination
			and transport type for AX25 callsigns.
			syntax: route <callsign> <hostname> [udp] [udp-port]
			For default route <callsign> is substituted by
			'default'. 
			Note: If default route is defined, no data will use
			an available KISS interface!

sample tfkiss.cfg file:
# Sample tfkiss/ax25ip configuration file
#
# First select active socket types
# syntax: socket <ip/udp> [udp-port]
#
socket ip
socket udp
#
# Select the mode of operation. (digi or tnc)
#
mode tnc
#
# If you selected digi, you must define a callsign.  If you selected
# tnc mode, the callsign is optional
#
mycall nocall
#
# loglevel 0 - no output
# loglevel 1 - config info only
# loglevel 2 - major events and errors
# loglevel 3 - major events, errors, and AX25 frame trace
# loglevel 4 - all events
#
loglevel 0
#
# Define some routes.  One example routes all traffic for callsign db0zzz
# to a host named nexthost.bla.blub.  You can define as many as
# required.
# syntax: route <callsign> <hostname> [udp] [udp-port]
#
route db0zzz nexthost.bla.blub
route db0zzy-5 otherhost.bla.blub udp
route db0zzx-2 localhost udp 10094
#
# A catch-all is provided: this line sends all calls not specifically
# noted in the routing tables to otherhost.bla.blub.  Use this feature
# with great care -- the host on the other end may not appreciate all the
# traffic!
# syntax: route default <hostname> [udp] [udp-port]
#
#route default otherhost.bla.blub
#
<EOF>


2. Options at startup
---------------------
Some options can be given at startup of tfkiss to change the behaviour
of the program.

Usage : tfkiss [-i <init-file>] [-s <tfkiss-socket>] [-u] [-r] [-t]

a) -i	defines a different init-file instead of tfkiss.ini
b) -s	defines a socket for the interface with TNT, even if tfkiss_socket
	is not defined
c) -u	ignores an existing lockfile for the KISS device
d) -r	ignore and delete all parameter values stored in tfkiss_parafile
e) -t	startup on console instead of using the socket to TNT, even
	if tfkiss_socket is defined

3. Finish TFKISS
----------------
To finish TFKISS two ways are possible:
In terminal mode give the command QRES, which, in contrast to the original
TNC-software, will only terminate the program, all parameter values like
callsign, txdelay, e.t.c. will be saved in tfkiss_parafile for the next
run.
If the socket interface to TNT is used, simply send a SIGTERM signal to
the process ('kill <tfkiss-process-ID>').


4. Extensions to TheFirmware
----------------------------
4.1. Parameter for txtail-length
--------------------------------
In KISS mode a value for the time between the last character put in the
HDLC controller and the switch off of the transmitter can be given.
This time is called 'txtail'.
It can be handled by the new extended TNC command '@TA'. The metric of
the value is 10ms, 4 means a txtail of 40ms.
 
4.2. Parameter for changing PID
-------------------------------
For special applications, like broadcast or TCP/IP different PID values
are needed. The PID can be changed using the new extended TNC command '@P'.
The argument for this command is the PID value in decimal. The PID will
be changed only on the currently selected channel.

4.3. Information about a changed PID
------------------------------------
If the remote station use a different PID than the default one 240 (0f0h),
a link status message will inform about this:
   'PID changed to (EF)'

4.4. Decoding of frames in internal FLEXNET protocol
----------------------------------------------------
FLEXNET digipeaters use a special format for communication. Only one address
field (7 Bytes) is used to define source and destination of the data.
This specially encoded address field is displayed in readable form.


5. Contact
----------
If you want to get in contact with me use the following ways:
HAM RADIO: DL4YBG @ DB0GR.#BLN.DEU.EU
E-Mail:    wahlm-at-berlin-snafu-de
Internet:  http://www.snafu.de/~wahlm/

73, Mark, DL4YBG